## Slide 1: Unit – III Network Essentials
Network Models

## Slide 2: OSI Model
Open Systems Interconnection (OSI) is a set of internationally recognized, non-proprietary standards for networking and for operating system involved in networking functions.
7 Layers
7. Application Layer
6. Presentation Layer
5. Session Layer
4. Transport Layer
3. Network Layer
2. Data Link Layer
1. Physical Layer

## Slide 3
ISO is the organization. OSI is the model.
Note

## Slide 4
Figure 2.4 OSI layers

## Slide 5
Figure 2.5 An exchange using the OSI model

## Slide 6: Layer Architecture
Layer architecture simplifies the network design.
It is easy to debug network applications in a layered architecture network.
The network management is easier due to the layered architecture.
Network layers follow a set of rules, called protocol.
The protocol defines the format of the data being exchanged, and the control and timing for the handshake between layers.
OSI Model

## Slide 7
The physical layer is responsible for movements of
individual bits from one hop (node) to the next.
Note

## Slide 8: Physical Layer
Provides physical interface for transmission of information.
The physical layer is responsible for movements of individual bits from one hop (node) to the next.
This layer tells the driver software for the MAU (media attachment unit, ex. network interface cards (NICs, modems, etc.)) what needs to be sent across the medium.
This layer manages the interface between the the computer and the network medium (coax, twisted pair, etc.)
Defines rules by which bits are passed from one system to another on a physical communication medium.
Covers all - mechanical, electrical, functional and procedural - aspects for physical communication.
Such characteristics as voltage levels, timing of voltage changes, physical data rates, maximum transmission distances, physical connectors, and other similar attributes are defined by physical layer specifications.
OSI Model

## Slide 9
The data link layer is responsible for moving frames from one hop (node) to the next.
Note

## Slide 10: Data Link Layer
Data link layer attempts to provide reliable communication over the physical layer interface.
Breaks the outgoing data into frames and reassemble the received frames.
Create and detect frame boundaries.
Handle errors by implementing an acknowledgement and retransmission scheme.
Implement flow control.
Supports points-to-point as well as broadcast communication.
Supports simplex, half-duplex or full-duplex communication.
OSI Model

## Slide 11
The network layer is responsible for the delivery of individual packets from
the source host to the destination host.
Note

## Slide 12: Network Layer
Implements routing of frames (packets) through the network.
Defines the most optimum path the packet should take from the source to the destination
Defines logical addressing so that any endpoint can be identified.
This layer also handles packet switching and network congestion control
Facilitates interconnection between heterogeneous networks (Internetworking).
The network layer also defines how to fragment a packet into smaller packets to accommodate different media.
OSI Model

## Slide 13
The transport layer is responsible for the delivery of a message from one process to another.
Note

## Slide 14: Transport Layer
Purpose of this layer is to provide a reliable mechanism for the exchange of data between two processes in different computers.
Manages the flow of data between parties by segmenting long data streams into smaller data chunks (based on allowed “packet” size for a given transmission medium).
Ensures that the data units are delivered error free.
Ensures that data units are delivered in sequence.
Ensures that there is no loss or duplication of data units.
Provides connectionless or connection oriented service.
Provides for the connection management.
Multiplex multiple connection over a single channel.
OSI Model

## Slide 15
The session layer is responsible for dialog control and synchronization.
Note

## Slide 16: Session Layer
Session layer provides mechanism for controlling the dialogue between the two end systems. It defines how to start, control and end conversations (called sessions) between applications.
This layer requests for a logical connection to be established on an end-user’s request.
Any necessary log-on or password validation is also handled by this layer.
Session layer is also responsible for terminating the connection.
This layer provides services like dialogue discipline which can be full duplex or half duplex.
Session layer can also provide check-pointing mechanism such that if a failure of some sort occurs between checkpoints, all data can be retransmitted from the last checkpoint.
OSI Model

## Slide 17
The presentation layer is responsible for translation, compression, and encryption.
Note

## Slide 18: Presentation Layer
Presentation layer defines the format in which the data is to be exchanged between the two communicating entities.
This layer is also responsible for certain protocol conversions, data encryption/decryption, or data compression/decompression
Also handles data compression and data encryption (cryptography).
OSI Model

## Slide 19
The application layer is responsible for providing services to the user.
Note

## Slide 20: Application Layer
Application layer interacts with application programs and is the highest level of OSI model.
Application layer contains management functions to support distributed applications.
Provides a set of interfaces for sending and receiving applications and to use network services, such as: message handling and database query processing
Responsibility: It provides the services to the user.
Examples of application layer are applications such as file transfer, electronic mail, remote login etc.
OSI Model

## Slide 21: OSI in Action
A message begins at the top application layer and moves down the OSI layers to the bottom physical layer.
As the message descends, each successive OSI model layer adds a header to it.
A header is layer-specific information that basically explains what functions the layer carried out.
Conversely, at the receiving end, headers are striped from the message as it travels up the corresponding layers.
OSI Model

## Slide 22
Summary

## Slide 23
TCP/IP Model
TCP/IP MODEL

## Slide 24
What is TCP/IP?
TCP/IP is a set of protocols developed to allow cooperating computers to share resources across a network
TCP stands for “Transmission Control Protocol”
IP stands for “Internet Protocol”
They are Transport layer and Network layer protocols respectively of the protocol suite
The most well known network that adopted TCP/IP is Internet – the biggest WAN in the world

## Slide 25
A protocol is a collection of rules and procedures for two computers to exchange information
Protocol also defines the format of data that is being exchanged
What is a protocol?

## Slide 26
Why TCP/IP is so popular?
TCP/IP was developed very early
Technologies were widely discussed and circulated in documents called “Request for Comments” (RFC) – free of charge
Supported by UNIX operating system

## Slide 27: OSI & TCP/IP Models
TCP/IP Model

## Slide 28: TCP/IP Model
TCP/IP Model
Application Layer
Application programs using the network
Transport Layer (TCP/UDP)
Management of end-to-end message transmission,
error detection and error correction
Network Layer (IP)
Handling of datagrams : routing and congestion
Data Link Layer
Management of cost effective and reliable data delivery,
access to physical networks
Physical Layer
Physical Media

## Slide 29: TCP/IP and OSI model

## Slide 30: Relationship of layers and addresses in TCP/IP

## Slide 31
Application layer protocols define the rules when implementing specific network applications
Rely on the underlying layers to provide accurate and efficient data delivery
Typical protocols:
  FTP – File Transfer Protocol
    For file transfer
  Telnet – Remote terminal protocol
    For remote login on any other computer on the network
  SMTP – Simple Mail Transfer Protocol
    For mail transfer
  HTTP – Hypertext Transfer Protocol
    For Web browsing
Layer-1 Application Layer

## Slide 32
Layer-2 Transport Layer
Application
Transport
Network
Network Interface
Message
Segments
h
M
h
M
h
M

## Slide 33
TCP and UDP
TCP is a connection-oriented protocol
  Does not mean it has a physical connection between sender and receiver
  TCP provides the function to allow a connection virtually exists – also called virtual circuit
TCP provides the functions:
  Dividing a chunk of data into segments
  Reassembly segments into the original chunk
  Provide further the functions such as reordering and data resend
Offering a reliable byte-stream delivery service
TCP – Transmission Control Protocol

## Slide 34
Layer-3 Network Layer
Application
Transport
Network
Network Interface
Message
Segments
h
M
h
M
h
M
h
M
h
h
M
h
h
M
h
Datagrams / Packets

## Slide 35
Network Addresses and Subnets
A header is added to each segment in the Network layer
IP
3
 |  | Total Length
Time to Live | Protocol | Header CheckSum
Source Address |  | 
Destination Address |  | 
Segment |  | 
Segment

## Slide 36
Layer-4 Data Link and Physical Layers
Application
Transport
Network
Network Interface
Message
Segments
h
M
h
M
h
M
h
M
h
h
M
h
h
M
h
Packets
h
M
h
h
M
h
h
h
Frames